## Slide 2: Types of Contaminants in Fresh Water
Loading
How much of the contaminant is added to water
Physical, Chemical and Biological Transformation
Reactions in water leading to formation/destruction of contaminants
Physical Transport, i.e., Mass Transport
How the contaminant is spread in the water
Mass Transfer
  Transfer of contaminant from water to soil and air
1. Dissolved / particulate
2. Organic / inorganic
Factors Determining Concentration of Contaminants

## Slide 3
Biological / chemical processes involving dissolved contaminants
Acid-Base Reaction organic / inorganic
Complexation Reaction organic / inorganic
Precipitation Reaction inorganic
Oxidation-Reduction organic / inorganic
Hydrolysis mostly organic (will be briefly discussed)
Photolysis mostly organic (will be briefly discussed)
Biodegradation mostly organic (will be briefly discussed)
Physical processes involving particulate contaminants
Sedimentation
Coagulation / flocculation
Filtration
3. Mass transport of dissolved / particulate contaminants
Advection
Diffusion / Dispersion
Mass transfer of dissolved contaminants
Solid-liquid mass transfer adsorption / desorption
Gas-liquid mass transfer absorption / stripping
Processes Undergone by Contaminants in Water

## Slide 5
General Properties of Water
Formula: H2O
Molecular Mass: 18 g / mole
Density: 1000 kg/m3
Polarity of Water
Water is a polar molecule. The extremity of the molecule having oxygen atom has an excess negative charge. The other two extremities have excess positive charge.
Hydrogen Bonds
The negative parts of a water molecule are attracted to the positive parts of other water molecules, i.e., they form hydrogen bonds.
Each water molecule can form up to 4 hydrogen bonds. This is the reason why water molecules stick to each other and form droplets.
Structure of Water
Three-dimensional depiction of the structure of water shows large void spaces between molecules.
Water as a Solvent
Due to its polarity, hydrogen bond forming ability and also due to the presence of large void spaces between molecules, water can dissolve a large variety of ionic and polar compounds.

## Slide 6
Acid-Base Chemistry
Acid: An acid is any chemical, which when added to pure water (pH = 7) results in a pH decrease.
This means that addition of an acid to water results in the increase in the concentration of H+ ions in water (and corresponding decrease in OH- ion concentration). Remember, [H+].[OH-] = 10-14 always.
Base: A base is any chemical, which when added to pure water (pH = 7) results in a pH increase.
This means that addition of a base to water results in the increase in the concentration of OH- ions in water (and corresponding decrease in H+ ion concentration).
Strong Acid: A strong acid, when added to water is completely dissociated, producing an equivalent quantity of H+ ions.
HCl is a strong mono-protic acid. When added to water, it completely dissociates, releasing equivalent quantity of H+ ions, . So if 1 mole of HCl is added to water, 1 mole of H+ and 1 mole of Cl- will be released into the water. No HCl will remain in the water.
is a strong bi-protic acid. , so if 1 mole of is added to water, 2 moles of H+ and 1 mole of will be released into water. No will remain in water.

## Slide 7
What is the Concentration of Water in Water ??
1-liter of water weighs 1000 g.
1 gm-mole of water = 18 g
No. of gm-moles in 1-liter of water = 1000/18 =55.55
Hence, concentration of water in water is 55.55 M
However, the above statement is not completely correct, since pure water is partially dissociated as below,
Since water is electrically neutral, [H+] = [OH-] = 10-7 M
Hence, pH of pure water is 7.

## Slide 8
Strong Base: A strong base, when added to water is completely dissociated, producing an equivalent quantity of OH- ions.
NaOH is a strong base. When added to water, it completely dissociates, releasing equivalent quantity of OH- ions, . So if 1 mole of NaOH is added to water, 1 mole of OH- and 1 mole of Na+ will be released into the water. No NaOH will remain in the water.
Example Problem:
What is the pH of 10-3 M HCl solution ?
[Cl-] = 10-3 M
[H+].[OH-] = 10-14
Charge Balance: [H+] = [OH-] + [Cl-]
pH = 3

## Slide 9: Class Problem
On a piece of paper provided to you, please answer the following question. Write your name and roll number before submitting the sheet today.
What is the pH of 10-2 M H2SO4?
What is the pH of 10-3 M NaOH?

## Slide 10
Example Problem:
What is the pH of 10-8 M HCl solution ?
[Cl-] = 10-8 M
[H+].[OH-] = 10-14
Charge Balance: [H+] = [OH-] + [Cl-]
pH = 6.978
Solve the following problems:
What is the pH of 10-4 M H2SO4 solution?
What is the pH of 10-8 M NaOH solution?

## Slide 12: Relative Sizes of Environmental Constituents

## Slide 13: Residence Times of Water Molecules

## Slide 15: Environmental Issues of Inorganic Contaminants in India
Excessive Fluoride in Groundwater
Source: Chakraborti et al. ES&T 2011
Carcinogenic Arsenic in Groundwater
Source: Chakraborti et al. ES&T 2011
Uranium Processing and Long-term Storage
Source: K.M. Gunderson

## Slide 16
Historical Perspective on Groundwater Quality Management in India
Source: Chakraborti et al. Environmental Science and Technology (2011)
~1940s: Water from surface water sources like rivers, ponds, rainwater, etc.
Mid 20th century challenges:
Shortage of food due to excessive population growth
Prevalence of water-borne diseases like cholera, dysentery, etc. (GOI Environmental Hygience Commmitte, 1949)
Need for Groundwater sources for agricultural and domestic water needs
Early 1960s: Expansion in groundwater use due to electrical subsidies, decreasing tubewell costs, financial credit availability Green Revolution
WHO and UNICEF proposed use of groundwater for safe drinking water
1969: National Rural Drinking Water Supply Programme was launched
2005: Bharat Nirman Programme to develop rural drinking water and irrigation systems; every household targeted by 2009 (still to be realized)
Source: Chakraborti et al. Environmental Science and Technology (2011)

## Slide 17
Groundwater Use and Major Pollutants…1
Source: Chakraborti et al. Environmental Science and Technology (2011)
Usage: ~80 % of rural India and ~50% of urban India for domestic purposes
~33% of country’s groundwater resources are unfit for consumption (TOI, Mar 2010)
Anthropogenic Contaminant Sources:
Sewage Disposal: Bacteria (only ~10 % of urban sewage is treated), Nitrate
Agriculture: Nitrate (11 of 28 States in India and ~22% of villages in Rajasthan have more than 45 ppm)
Pesticide (long-term source)
Industry: Heavy Metals (Cr, Cd, Ni, Hg, As); Organics through untreated discharge Waste from Paris-Green insecticide production caused As contamination in Kolkata (1993); Chromite ore processing residue in areas near Kanpur and Chennai;

## Slide 18
Groundwater Use and Major Pollutants…2
Geogenic Contaminant Sources:
Fluoride: Fluorosis is the most prevalent groundwater-related disease in India (the most severely affected country worldwide)
~66 million people affected in India; ~20 States have some districts
Arsenic: Primarily in the floodplains of Ganga-Brahmaputra Plains
Iron: Largest pollutant among heavy metals
Salinity (predominantly, Cl- salts): due to seawater ingress in coastal areas
inappropriate agricultural practices
Source: Chakraborti et al. Environmental Science and Technology (2011)